## Slide 1: Virtual Memory: Systems Introduction to Computer Systems 21st Lecture, Nov. 30, 2015
Instructors:
Xiangqun Chen，Junlin Lu
Guangyu Sun，Xuetao Guan

## Slide 2: Today
Virtual memory questions and answers
Simple memory system example
Bonus: Memory mapping
Bonus: Case study: Core i7/Linux memory system

## Slide 3: Virtual memory reminder/review
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions

## Slide 4: Recall: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table
Page table base register
(PTBR)
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
Physical page offset (PPO)
0
p-1
Physical page number (PPN)
p
m-1

## Slide 5: Recall: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 6: Question #1
Are the PTEs cached like other memory accesses?
Yes (and no: see next question)

## Slide 7: Page tables in memory, like other data
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 8: Question #2
Isn’t it slow to have to go to memory twice every time?
Yes, it would be… so, real MMUs don’t

## Slide 9: Speeding up Translation with a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small, dedicated, super-fast hardware cache of PTEs in MMU
  Contains complete page table entries for small number of pages

## Slide 10: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 11: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?

## Slide 12: Question #3
Aren’t the TLB contents wrong after a context switch?
Yes, they would be, so something must be done..
  Option 1: flush TLB on context switch
  Option 2: associate a process ID with each TLB entry

## Slide 13: Question #4
Isn’t the page table huge? How can it be stored in RAM?
Yes, it would be… so, real page tables aren’t simple arrays

## Slide 14: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 64-bit address space, 8-byte PTE
Problem:
  Would need a 32,000 TB page table!
    264 * 2-12 * 23 = 255 bytes
Common solution:
  Multi-level page tables
  Example: 2-level page table
    Level 1 table: each PTE points to a page table (always memory resident)
    Level 2 table: each PTE points to a page (paged in and out like any other data)
Level 1
Table
...
Level 2
Tables
...

## Slide 15: A Two-Level Page Table Hierarchy
Level 1
page table
...
Level 2
page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
32 bit addresses, 4KB pages, 4-byte PTEs

## Slide 16: Translating with a k-level Page Table
VPN-1
0
p-1
n-1
VPO
VPN-2
...
VPN-k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table

## Slide 17: Question #5
Shouldn’t fork() be really slow, since the child needs a copy of the parent’s address space?
Yes, it would be… so, fork() doesn’t really work that way

## Slide 18: Physical memory can be shared
Process 1 maps the shared pages
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 19: Physical memory can be shared
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the shared pages
Notice how the virtual addresses can be different

## Slide 20: Private Copy-on-write (COW) sharing
Two processes mapping private copy-on-write (COW) pages
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 21: Private Copy-on-write (COW) sharing
Instruction writing to private page triggers protection fault
Handler creates new R/W page
Instruction restarts upon handler return
Copying deferred as long as possible!
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 22: The fork Function Revisited
fork provides private address space for each process
To create virtual address for new process
  Create exact copies of parent page tables
  Flag each page in both processes (parent and child) as read-only
  Flag writeable areas in both processes as private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new physical pages using COW mechanism
Perfect approach for common case of fork() followed by exec()
  Why?

## Slide 23: Today
Virtual memory questions and answers
Simple memory system example
Bonus: Memory mapping
Bonus: Case study: Core i7/Linux memory system

## Slide 24: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  VPO: Virtual page offset
  VPN: Virtual page number
  TLBI: TLB index
  TLBT: TLB tag
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 25: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 26: Simple Memory System Page Table
Only show first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN

## Slide 27: Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set

## Slide 28: Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 29: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36
Notes: 都在cache,事实上没有访存

## Slide 30: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0
0x2E
2
0x0B
N
Y
TBD

## Slide 31: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 32: Today
Virtual memory questions and answers
Simple memory system example
Bonus: Memory mapping
Bonus: Case study: Core i7/Linux memory system

## Slide 33: Memory Mapping
VM areas initialized by associating them with disk objects.
  Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate a physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 34: Demand paging
Key point: no virtual pages are copied into physical memory until they are referenced!
  Known as demand paging
Crucial for time and space efficiency

## Slide 35: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
  start: may be 0 for “pick an address”
  prot: PROT_READ, PROT_WRITE, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)

## Slide 36: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 37: Using mmap to Copy Files
#include "csapp.h"
/*
* mmapcopy - uses mmap to copy
* file fd to stdout
*/
void mmapcopy(int fd, int size)
{
/* Ptr to mem-mapped VM area */
char *bufp;
bufp = Mmap(NULL, size,
PROT_READ,
MAP_PRIVATE, fd, 0);
Write(1, bufp, size);
return;
}
/* mmapcopy driver */
int main(int argc, char **argv)
{
struct stat stat;
int fd;
/* Check for required cmdline arg */
if (argc != 2) {
printf("usage: %s <filename>\n”,
argv[0]);
exit(0);
}
/* Copy the input arg to stdout */
fd = Open(argv[1], O_RDONLY, 0);
Fstat(fd, &stat);
mmapcopy(fd, stat.st_size);
exit(0);
}
Copying without transferring data to user space .

## Slide 38: Today
Virtual memory questions and answers
Simple memory system example
Bonus: Memory mapping
Bonus: Case study: Core i7/Linux memory system

## Slide 39: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge
Notes: 4kb*8way=32kb
这里TLB整棵树都存，和实现有关。

## Slide 40: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 41: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE
Notes: 这里都没有讲权限的问题。
可能前几级，不是叶子就发现invalid了

## Slide 42: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
CD: Caching disabled or enabled for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 3 PTEs only).
G: Global page (don’t evict from TLB on task switch)
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63

## Slide 43: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
CD: Cache disabled (1) or enabled (0)
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
G: Global page (don’t evict from TLB on task switch)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 44: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 45: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available next
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
36
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 46: Virtual Memory of a Linux Process
Kernel code and data
Memory mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%esp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x08048000 (32)
0x00400000 (64)
Different for each process

## Slide 47: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
vm_flags
vm_flags
vm_flags

## Slide 48: Linux Page Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a non-existing page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)

## Slide 49: The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
  Programs and initialized data backed by object files.
  .bss and stack backed by anonymous files .
Set PC to entry point in .text
  Linux will fault in code and data pages as needed.
Memory mapped region
for shared libraries
Runtime heap (via malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
Private, demand-zero
libc.so
.data
.text
Shared, file-backed
Private, demand-zero
Private, demand-zero
Private, file-backed
a.out
.data
.text